Temperature solver

Assuming temperature steady state (where dT over dt = 0 ), the conservation of energy with no transient and no radiation heat transfer yields
P_i - P_conv - P_cond = 0 , where:
P_i [ W ] is the internal generated heat computed by the electrical solver
P_conv [ W ] is the outwards flowing (front and back) convection heat
P_cond [ W ] is the outwards flowing (sideways) conduction heat to or from each neighboring element

# Internal generated power
This part of the equation was computed by the previous solver and is assumed to be constant for each element:
P_i = iiint from{partial %OMEGA} %sigma {abs vec{E}}^2 d %OMEGA
# Convection heat transfer
The convective heat is assumed to flow to the back (into the screen) and to the front (out of the screen). It relies on the given global and constant ambient temperature T_amb [ K ] and on the elemental convection heat resistance R_conv [ K/W ] , which depends on the triangular area of the element A [ m² ] and on the convective heat transfer coefficients h_back and h_front left[ W over {m²K} right]
P_conv = R_conv cdot ( T - T_amb ) , R_conv = A^-1 cdot (h_back + h_front )^-1 color red{ + A_{free edge}^-1 (h_back + h_front )/2 } , color red {A_{free edge } approx 0 " for relatively thin depth"}
# Conduction heat transfer
The conduction heat happens among the elements on the plane. Each element may have up to 3 neighbors indexed as l = 0, 1, 2 . The conduction thermal resistance R_l [ K/W ] is proportional to the distance %DELTA x [ m ] between the elements centroids and to the inverse of the interface area A_s [ m² ] and the thermal conductivity k [ W/mK ]
P_cond = sum from{l=0} to{2} R_l^-1 cdot ( T - T_l ) , R_l = { %DELTA x } over { k A_s} , "pseudo-python: " %DELTA x = "element.distance_to"("neighbor")
A_s = (depth) cdot (edge length)
# Element heat equation
For each element in the domain, the corresponding equation is therefore.
left( R_conv^-1 + sum from{l=0} to{2} R_l^-1 right) T - sum from{l=0} to{2} R_l^-1 T_l= P_i + R_conv^-1 T_amb
If a neighbor is missing (i.e. if the element is in a border and no neighbor is defined), the corresponding sum parcel must be omitted. E.g. if the triangular element is in the corner of a square geometry and has only one neighbor, l=0 (iterates only once). If this element was in an linear edge, two neighbors would be present and l=0, 1 .
## Example
A domain of three elements shown below is presented.

left lbrace matrix{ left( R_conv0^-1 + R_01 right) T - R_01 T_1= P_i0 + R_conv0^-1 T_amb ## ... ## ... } right rbrace
For 3 elements we have a set of 3 equations with 3 unknowns, leading to a 3x3 system:
bold A cdot bold T = bold B
left[ matrix{ R_conv0^-1 + R_01^-1 # -R_01^-1 # 0 ## -R_10^-1 # R_conv1^-1 + R_10^-1 + R_12^-1 # -R_12^-1 ## 0 # -R_21^-1 # R_conv2^-1 + R_21^-1 } right ] cdot left[ matrix{ T_0 ## T_1 ## T_2 } right] = left[ matrix{ P_0+R_conv0^-1 T_amb ## P_1+R_conv1^-1 T_amb ## P_2+R_conv2^-1 T_amb } right]
The solution is thus
bold T = bold A^-1 cdot bold B